## Slide 1: Smart Plant Monitoring System
Group Members:
23_NTU_CS-1257(Laiba Fatima)
23_NTU_CS-1259(Mahnoor Sajjad)
BSAI-5th

## Slide 2: Introduction
Plants require regular watering and monitoring
Manual watering is inefficient and time-consuming
IoT provides an automated and smart solution

## Slide 3: Project Objectives
Monitor temperature and humidity
Detect soil moisture level
Sends data to Blynk app and MQTT broker
Automatically control water pump
Monitor and control system remotely
Displays data on OLED screen

## Slide 4: Problem Statement
Over-watering wastes water
Under-watering damages plants
Manual monitoring is not reliable

## Slide 5: Proposed Solution
ESP32 continuously reads sensor data,
Soil condition decides motor ON/OFF
Real-time data sent to Blynk App and MQTT broker

## Slide 6: Hardware Components
ESP32 NodeMCU-32S
DHT11 Temperature & Humidity Sensor
Soil Moisture Sensor (Analog)
Relay Module & Water Pump
OLED Display (128x64)

## Slide 7: Software & Libraries
Arduino Framework
Blynk IoT Platform
Adafruit SSD1306 & GFX Libraries
DHT Sensor Library
Wifi and MQTT broker
Node-Red/ MQTT broker

## Slide 8: Pin Configuration
DHT11 Data Pin → GPIO 27
Soil Sensor Analog Pin → GPIO 34.
Relay Control Pin → GPIO 26
OLED SDA → GPIO 21
OLED SCL → GPIO 22

## Slide 9: Sensors Working
DHT11 measures temperature and humidity
Soil sensor provides moisture value
ESP32 processes sensor data

## Slide 10: OLED Display Output
Temperature (°C)
Humidity (%)
Soil moisture value
Soil status: DRY or WET

## Slide 11: Blynk IoT Dashboard
V0: Temperature
V1: Humidity
V2: Soil Moisture
V3: Motor ON/OFF switch
V4: Soil status LED

## Slide 12: Manual Control Using Blynk
User can manually control motor
Switch widget used in Blynk App
Manual control overrides auto mode

## Slide 13: MQTT Integration
Broker: Mosquitto on PC (IP: 192.168.0.107, Port: 1883)
Topics:
smartplant/temp → Temperature
smartplant/hum → Humidity
smartplant/soil → Soil
smartplant/motor → Motor state
ESP32 publishes readings every 3s.
Can connect Node-RED dashboard for monitoring
.

## Slide 14: Node-Red Dashboard
ESP32 publishes MQTT messages.
Node-RED subscribes to topics.
Dashboard shows:
Temperature
Humidity
Soil Moisture
Motor Status

## Slide 15: Automatic Watering Logic
If soil value is below threshold
Soil is DRY → Motor turns ON
If soil value is above threshold
Soil is WET → Motor turns OFF

## Slide 16: Soil Moisture Threshold
Threshold value is set to 500
If soil value < 500 → Soil is DRY
If soil value ≥ 500 → Soil is WET
Threshold helps decide automatic motor ON/OFF

## Slide 17: System Workflow
Read sensors
Display data on OLED
Send data to Blynk App and MQTT broker
Check soil condition
Control water pump

## Slide 18: SYSTEM FLOW DIAGRAM
Start System
Read Sensors (DHT11 & SOIL)
Display Data on OLED
Send Data to blynk app and MQTT broker
Check Soil moisture level
Motor ON / OFF (Auto Watering)

## Slide 19: Advantages
Fully automatic watering system
Saves water and energy
Real-time monitoring
Easy and user-friendly

## Slide 20: Applications
Home gardening
Greenhouses
Smart agriculture
Indoor plant monitoring

## Slide 21: Future Enhancements
Capacitive soil moisture sensor
Mobile notifications
Solar power integration
Cloud data logging

## Slide 22: Conclusion
Smart and efficient plant care system
Reduces human effort
Demonstrates effective use of IoT and ESP32
Monitors temperature, humidity, soil moisture in real-time.
Provides visual feedback via OLED and Blynk
MQTT allows remote monitoring & integration with dashboards.